## Slide 1
MQTT WORKFLOW
MQTT BROKER
(VerneMQ)
Platform
(Subscriber)
DB
AMS Device
Simulator
(Publisher)
Google Protocol Buffer
AMS Device
Simulator
(Publisher)
AMS Device
Simulator
(Publisher)
Notes: How MQTT works? - Slide 6
How Protobuf works? - Slide 7

## Slide 2
How MQTT Works?

## Slide 3
Publish, Subscribe & Persist
AMS client (Publisher) connects to the broker, decode the message in protobuf and publishes it to a specific topic (e.g. ams/device/process)
Google Protocol Buffer
Broker receives the message from the ams client and sends it to the clients which are subscribed to that topic.
(DB client in our case)
Another client (Subscriber) connects and subscribes to the topic (ams/#) and receives the protobuf from the broker and encode it to get the message and finally persist it to the db if required.
DB

## Slide 4: Two way syncing
Workflow

## Slide 5: Case - 1
When process(es) is/are created on AMS Device

## Slide 6
PID | updated_on | status | plat_pid
01 | 06-05-19 12:00 | 1 | null
AMS 1001
Pid | updated_on | status
null | null | null
1. AMS device publishes a list containing
process(es) which have status = 1
sync/process
Topic
2. Platform checks if the list is empty or
not. If not empty, check if process
exists in process_master table or not
with plat_pid.
3. If process(es) not exist(s) in table,
platform insert process(es) into
process_master
Pid | updated_on | status
P01 | 06-05-19 12:00 | 1
PLATFORM
PLATFORM
PID | updated_on | status | plat_pid
01 | 06-05-19 12:00 | 0 | P01
AMS 1001
4. Platform publishes all the processes
which has status = 1 with pair of
Pid-PID to the ams
ams/sync/process/{clientId}
5. AMS updates plat_pid, set status to 0
and publishes acknowledgement to
the platform with its clientId
sync/ack/process
id | last_synced_on | clientId | synced
1 | 08-05-19 14:30 | 1001 | 1
ams_process_sync_log
6. AMS sync date saved
in the log table with
synced status set to 1.

## Slide 7: Case - 2
When process(es) is/are created on Platform

## Slide 8
PID | updated_on | status | plat_pid
null | null | null | null
AMS 1001
Pid | updated_on | status
PR-01 | 06-05-19 12:00 | 1
1. AMS device publishes a list containing
process(es) which have status = 1
sync/process
Topic
2. Platform checks if the list is empty or
not. If empty, check if ams has been
synced before or it is the first time.
3. If ams sync log does not exists,
platform publishes all the processes
to the ams device.
PLATFORM
PID | updated_on | status | plat_pid
01 | 06-05-19 12:00 | 0 | P01
AMS 1001
ams/sync/process/{clientId}
4. AMS inserts the received process(es),
set status to 0 and publishes
acknowledgement to the platform with
its clientId
sync/ack/process
id | last_synced_on | clientId | synced
1 | 08-05-19 14:30 | 1001 | 1
ams_process_sync_log
5. AMS sync date saved
in the log table with
synced status set to 1.
Notes: MODIFICATION:
AMS: If ams device failed to update the changes, then it will send acknowledgment with received flat set to false to topic: sync/ack/process
PLATFORM: If received = false, then platform sends a message to try again for the request on topic: error/sync/process

## Slide 9: Case - 3
When modification(s) is/are occurred on both sides

## Slide 10
PID | updated_on | status | plat_pid
01 | 07-05-19 12:00 | 1 | PR-01
02 | 07-05-19 15:30 | 1 | null
AMS 1001
Pid | updated_on | status
PR-01 | 06-05-19 12:00 | 1
PR-02 | 08-05-19 13:00 | 1
sync/process
Topic
1. AMS device publishes a list containing process(es) which
have status = 1
2. Platform checks for every process entity joining the plat_pid
to Pid in process_master.
3. If exists it checks if the status of sent ams process and the
one on platform are same or not.
4. In this case, they are not same, when both status = 1, it
checks which process entity has the latest modifications by
comparing update_on field.
5. In this case, modification has been done on ams side, so
the ams process entity will be reflected in platform’s
process_master table.
6. Process entity in ams with PID = 02 has plat_pid = null, so a
new row will be inserted in platform’s process_master
PLATFORM
Pid | updated_on | status
PR-01 | 07-05-19 12:00 | 1
PR-02 | 08-05-19 13:00 | 1
PR-03 | 07-05-19 15:30 | 1
PLATFORM
PART - 1 : AMS to Platform

## Slide 11
PID | updated_on | status | plat_pid
01 | 07-05-19 12:00 | 1 | PR-01
02 | 07-05-19 15:30 | 1 | null
AMS 1001
2. AMS updates all the processes, set status = 0 and
publishes acknowledgement to platform.
Pid | updated_on | status
PR-01 | 07-05-19 12:00 | 1
PR-02 | 08-05-19 13:00 | 1
PR-03 | 07-05-19 15:30 | 1
PLATFORM
PART - 2 : Platform to AMS
1. Platform publishes all the processes
which have status = 1 with PID-pid
pair map (if any insertion happens
otherwise blank PID-pid map)
ams/sync/process/{clientId}
PID | updated_on | status | plat_pid
01 | 07-05-19 12:00 | 0 | PR-01
02 | 07-05-19 15:30 | 0 | PR-03
03 | 08-05-19 13:00 | 0 | PR-02
AMS 1001
sync/ack/process
id | last_synced_on | clientId | synced
1 | 09-05-19 14:30 | 1001 | 1
ams_process_sync_log
3. AMS sync date saved
in the log table with
synced status set to 1.

## Slide 12: Some other cases: 1. If process needs to be deleted, then it should be soft delete (maintaining is_active flag) in the process_master table rather than deleting the row from the table. 2. Everytime acknowledgement is received from the ams, synced on date in ams_process_log table is updated and synced flag is set to 1. When all the ams devices are synced with the platform, then the status in platform’s process master will be changed to 0 which means that whole system is synced to each other.

## Slide 13: One way syncing
User(s) Workflow

## Slide 14
AMS
1. AMS device sends request for
users to platform.
sync/users/request
Topic
2. Platform checks if this ams is new to platform or it already exists. If it is a new ams, then platform will send all the users list to ams otherwise it sends list from ams last synced date to current date.
5. If ams does not exists in table,
Creates a new entry otherwise update
last_synced_on
PLATFORM
3. AMS device updates the users
list in the table.
ams/sync/users/{clientId}
response/users/1002
id | last_synced_on | clientId
1 | 08-05-19 14:30 | 1001
ams_users_sync
3. Platform sends a message if
device is already synced
to platform.’
sync/ack/users
3. Platform sends list of users
4. AMS sends acknowledgement.
If update successfully, set received
flag to true, else set false.
error/sync/users/{clientId}
received?
If received = true
If received = false
5. Sends a message to request again to
the ams device.

## Slide 15: One way syncing
Schedule(s) Workflow

## Slide 16
AMS
1. AMS device sends request for
Schedules to platform.
sync/schedules/request
Topic
2. Platform checks if this ams is new to platform or it already exists. If it is a new ams, then platform will send all the schedules list to ams otherwise it sends list from ams last synced date to current date.
5. If ams does not exists in table,
Creates a new entry otherwise update
last_synced_on
PLATFORM
3. AMS device updates the schedules
list in the table.
ams/sync/schedules/{clientId}
response/schedules/1002
id | last_synced_on | clientId
1 | 08-05-19 14:30 | 1001
ams_schedule_sync
3. Platform sends a message if
device is already synced
to platform.’
sync/ack/schedules
3. Platform sends list of schedules
4. AMS sends acknowledgement.
If update successfully, set received
flag to true, else set false.
error/sync/schedules/{clientId}
received?
If received = true
If received = false
5. Sends a message to request again to
the ams device.